# ESP-idf
## Serial comunication to pc and more:
platformio
to setup the monitoring in vscode and platformio add the line:

monitor_speed = 115200

to platformio.ini

to write from the esp32 to pc

#include <stdio.h>
void app_main(void)
{
printf("Hello world!\n");
}

to write from pc to esp32 for now:
while (1)
{
uint8_t ch;
ch = fgetc(stdin); // input non blocking
if (ch != 0xFF)
{
fputc(ch, stdout); // output
}
}

## upload to esp32 cam:
connect pin IO0 to ground and restart or plug in

## SD control:
The process is 3 steps process:
1. mount
2. use normal C file work
3. unmount

#### 1 – mount:

// objects
#include <string.h>
#include <sys/unistd.h>

//functions
#include <sys/stat.h> //for checking if file exist
#include "esp_vfs_fat.h"
#include "sdmmc_cmd.h"
#include "driver/sdmmc_host.h"

// static const char *TAG = "example";

#define MOUNT_POINT "/sdcard"

void app_main(void)
{
esp_err_t ret;

// Options for mounting the filesystem.
// If format_if_mount_failed is set to true, SD card will be partitioned and
// formatted in case when mounting fails.
esp_vfs_fat_sdmmc_mount_config_t mount_config = {
.format_if_mount_failed = false,
.max_files = 5, //Max number of open files
.allocation_unit_size = 16 * 1024};

sdmmc_card_t *card; //the object that will hold the card
const char mount_point[] = MOUNT_POINT; //name of card root pos

// Use settings defined above to initialize SD card and mount FAT filesystem.

sdmmc_host_t host = SDMMC_HOST_DEFAULT(); //the HW config data of the sd

// This initializes the slot without card detect (CD) and write protect (WP) signals.
// Modify slot_config.gpio_cd and slot_config.gpio_wp if your board has these signals.
sdmmc_slot_config_t slot_config = SDMMC_SLOT_CONFIG_DEFAULT();
slot_config.width = 4;

// Enable internal pullups on enabled pins.
slot_config.flags |= SDMMC_SLOT_FLAG_INTERNAL_PULLUP;

//the main mounting function:
//mount the card on card with mount_point position
ret = esp_vfs_fat_sdmmc_mount(mount_point, &host, &slot_config, &mount_config, &card);

if (ret != ESP_OK) //checks for errors
{
if (ret == ESP_FAIL)
{
//Failed to mount filesystem
}
else
{
//Failed to initialize the card -> esp_err_to_name(ret)
}
return;
}
// ********************************************* //

#### 2 – C filesystem:
// Use POSIX and C standard library functions to work with files:
// (normal C file usage)
// First create a file.
const char *file_hello = MOUNT_POINT "/hello.txt";

//Opening file
FILE *f = fopen(file_hello, "w");
if (f == NULL)
{
//Failed to open file for writing
return;
}
fprintf(f, "Hello %s!\n", card->cid.name);
fclose(f);
//File written

const char *file_foo = MOUNT_POINT "/foo.txt";

// Check if destination file exists before renaming
struct stat st;
if (stat(file_foo, &st) == 0)
{
// Delete it if it exists
unlink(file_foo);
}

// Rename original file
if (rename(file_hello, file_foo) != 0)
{
//Rename failed
return;
}

// Open renamed file for reading
f = fopen(file_foo, "r");
if (f == NULL)
{
//Failed to open file for reading
return;
}

// Read a line from file
char line[64];
fgets(line, sizeof(line), f);
fclose(f);

// Strip newline
char *pos = strchr(line, '\n');
if (pos)
{
*pos = '\0';
}
//******************************//

#### 3 – unmount:
// All done, unmount partition and disable SDMMC peripheral
esp_vfs_fat_sdcard_unmount(mount_point, card);
}

## camera control: