# ESP-idf
## Serial comunication to pc and more:
platformio
to setup the monitoring in vscode and platformio add the line:

monitor_speed = 115200

to platformio.ini

to write from the esp32 to pc

#include <stdio.h>
void app_main(void)
{
printf("Hello world!\n");
}

to write from pc to esp32 for now:
while (1)
{
uint8_t ch;
ch = fgetc(stdin); // input non blocking
if (ch != 0xFF)
{
fputc(ch, stdout); // output
}
}

## upload to esp32 cam:
connect pin IO0 to ground and restart or plug in

## SD control:
The process is 3 steps process:
1. mount
2. use normal C file work
3. unmount

#### 1 – mount:

// objects
#include <string.h>
#include <sys/unistd.h>

//functions
#include <sys/stat.h> //for checking if file exist
#include "esp_vfs_fat.h"
#include "sdmmc_cmd.h"
#include "driver/sdmmc_host.h"

// static const char *TAG = "example";

#define MOUNT_POINT "/sdcard"

void app_main(void)
{
esp_err_t ret;

// Options for mounting the filesystem.
// If format_if_mount_failed is set to true, SD card will be partitioned and
// formatted in case when mounting fails.
esp_vfs_fat_sdmmc_mount_config_t mount_config = {
.format_if_mount_failed = false,
.max_files = 5, //Max number of open files
.allocation_unit_size = 16 * 1024};

sdmmc_card_t *card; //the object that will hold the card
const char mount_point[] = MOUNT_POINT; //name of card root pos

// Use settings defined above to initialize SD card and mount FAT filesystem.

sdmmc_host_t host = SDMMC_HOST_DEFAULT(); //the HW config data of the sd

// This initializes the slot without card detect (CD) and write protect (WP) signals.
// Modify slot_config.gpio_cd and slot_config.gpio_wp if your board has these signals.
sdmmc_slot_config_t slot_config = SDMMC_SLOT_CONFIG_DEFAULT();
slot_config.width = 4;

// Enable internal pullups on enabled pins.
slot_config.flags |= SDMMC_SLOT_FLAG_INTERNAL_PULLUP;

//the main mounting function:
//mount the card on card with mount_point position
ret = esp_vfs_fat_sdmmc_mount(mount_point, &host, &slot_config, &mount_config, &card);

if (ret != ESP_OK) //checks for errors
{
if (ret == ESP_FAIL)
{
//Failed to mount filesystem
}
else
{
//Failed to initialize the card -> esp_err_to_name(ret)
}
return;
}
// ********************************************* //

#### 2 – C filesystem:
// Use POSIX and C standard library functions to work with files:
// (normal C file usage)
// First create a file.
const char *file_hello = MOUNT_POINT "/hello.txt";

//Opening file
FILE *f = fopen(file_hello, "w");
if (f == NULL)
{
//Failed to open file for writing
return;
}
fprintf(f, "Hello %s!\n", card->cid.name);
fclose(f);
//File written

const char *file_foo = MOUNT_POINT "/foo.txt";

// Check if destination file exists before renaming
struct stat st;
if (stat(file_foo, &st) == 0)
{
// Delete it if it exists
unlink(file_foo);
}

// Rename original file
if (rename(file_hello, file_foo) != 0)
{
//Rename failed
return;
}

// Open renamed file for reading
f = fopen(file_foo, "r");
if (f == NULL)
{
//Failed to open file for reading
return;
}

// Read a line from file
char line[64];
fgets(line, sizeof(line), f);
fclose(f);

// Strip newline
char *pos = strchr(line, '\n');
if (pos)
{
*pos = '\0';
}
//******************************//

#### 3 – unmount:
// All done, unmount partition and disable SDMMC peripheral
esp_vfs_fat_sdcard_unmount(mount_point, card);
}

-> one point: the led and data1 is shered on pin4
## camera control:
esp32-camera-github
first we need to clone the git and add it to the project or in platformio:
It's probably easier to just skip the platform.io library registry version and link the git repo as a submodule. (i.e. using code outside the platform.io library management). In this example we will install this as a submodule inside the platform.io $project/lib folder:
cd $project\lib
git submodule add -b master https://github.com/espressif/esp32-camera.git

Then in platformio.ini file

build_flags =
   -I../lib/esp32-camera
After that #include "esp_camera.h" statement will be available.

#### Usage:

#include "esp_camera.h"

#define CAM_PIN_PWDN -1 //power down is not used
#define CAM_PIN_RESET -1 //software reset will be performed
#define CAM_PIN_XCLK 21
#define CAM_PIN_SIODa 26
#define CAM_PIN_SIOC 27

#define CAM_PIN_D7 35
#define CAM_PIN_D6 34
#define CAM_PIN_D5 39
#define CAM_PIN_D4 36
#define CAM_PIN_D3 19
#define CAM_PIN_D2 18
#define CAM_PIN_D1 5
#define CAM_PIN_D0 4
#define CAM_PIN_VSYNC 25
#define CAM_PIN_HREF 23
#define CAM_PIN_PCLK 22

static camera_config_t camera_config = {
.pin_pwdn = CAM_PIN_PWDN,
.pin_reset = CAM_PIN_RESET,
.pin_xclk = CAM_PIN_XCLK,
.pin_sscb_sda = CAM_PIN_SIOD,
.pin_sscb_scl = CAM_PIN_SIOC,

.pin_d7 = CAM_PIN_D7,
.pin_d6 = CAM_PIN_D6,
.pin_d5 = CAM_PIN_D5,
.pin_d4 = CAM_PIN_D4,
.pin_d3 = CAM_PIN_D3,
.pin_d2 = CAM_PIN_D2,
.pin_d1 = CAM_PIN_D1,
.pin_d0 = CAM_PIN_D0,
.pin_vsync = CAM_PIN_VSYNC,
.pin_href = CAM_PIN_HREF,
.pin_pclk = CAM_PIN_PCLK,

.xclk_freq_hz = 20000000,
.ledc_timer = LEDC_TIMER_0,
.ledc_channel = LEDC_CHANNEL_0,

.pixel_format = PIXFORMAT_JPEG, //YUV422,GRAYSCALE,RGB565,JPEG
.frame_size = FRAMESIZE_UXGA, //QQVGA-QXGA Do not use sizes above QVGA when not JPEG

.jpeg_quality = 12, //0-63 lower number means higher quality
.fb_count = 1, //if more than one, i2s runs in continuous mode. Use only with JPEG
.grab_mode = CAMERA_GRAB_WHEN_EMPTY //CAMERA_GRAB_LATEST. Sets when buffers should be filled
};

esp_err_t camera_init()
{

//initialize the camera
esp_err_t err = esp_camera_init(&camera_config);
if (err != ESP_OK)
{
//Camera Init Failed
return err;
}

return ESP_OK;
}

esp_err_t camera_capture()
{
//acquire a frame
camera_fb_t *fb = esp_camera_fb_get();
if (!fb)
{
//Camera Capture Failed
return ESP_FAIL;
}
//replace this with your own function
//process_image(fb->width, fb->height, fb->format, fb->buf, fb->len);

//return the frame buffer back to the driver for reuse
esp_camera_fb_return(fb);
return ESP_OK;
}

video is just lots of pics together ;)

## wifi connectivity: